## Slide 1: ALMA: The Atacama Large Millimetre/submillimetre Array

## Slide 2
945+ publications since start of operations in 2011!

## Slide 3: ALMA Overview
A global partnership to deliver a revolutionary millimeter/submillimeter telescope array
  North America (US, Canada, Taiwan)
  Europe (ESO)
  East Asia (Japan,Taiwan)
  In collaboration with Chile
5000 m (16,500 ft) site in Chilean Atacama desert
66 telescopes in full operation
  Main Array: 50 x 12m antennas
  Total Power Array: 4 x 12m antennas
  Atacama Compact Array (ACA): 12 x 7m antennas
3
April 2013

## Slide 4: Where is ALMA?
Santiago
Paranal
La Serena
Atacama Desert,
Northern Chile

## Slide 5: Where is ALMA?

## Slide 6: Who is ALMA?
An international partnership between:
North America
Europe
Asia
Chile
to build the best possible submillimetre telescope

## Slide 7: Who is ALMA?
Standard ALMA acknowledgement:
“ALMA is a partnership of the European Southern Observatory (ESO; representing its member states), the National Science Foundation (NSF; USA) and the National Institutes of Natural Sciences (NINS; Japan), together with the National Research Council (NRC; Canada), the National Science Council (NSC; Taiwan) and the Academia Sinica Institute for Astronomy and Astrophysics (ASIAA; Taiwan), and the Korean Astronomy and Space Science Institute (KASI; Republic of Korea), in cooperation with the Republic of Chile. The Joint ALMA Observatory (JAO) is operated by ESO, the Associated Universities, Incorporated / the National Radio Astronomy Observatory (AUI/NRAO) and the National Astronomical Observatory of Japan (NAOJ)."

## Slide 8: ALMA Organization (Array Operations Site)
8
ALMA Technical Building (ATB)
Correlator
Llano de Chajnantor, Chile (elev. 5000 m)
latitude = −23.029°, longitude = −67.755°; elevation ~ 5000 m

## Slide 9: ALMA Organization (the Operations Support Facility)
9
Control Room
Dorms (facing west)
Control Building (elev. 2900 m)
c. Chat Hull
Casino

## Slide 10: ALMA Organization (Santiago Central Offices)
c. Chat Hull
c. ALMA
Elev. ~520 m
Sean Dougherty, ALMA Director

## Slide 11: ALMA Organization (ALMA Regional Centers)
NRAO Headquarters,
Charlottesville, VA, USA
NRC Herzberg
Victoria, BC, Canada
NA
EU
EA
+
c. ALMA
c. NRAO
c. NRC

## Slide 12: ALMA Data Flow
1. Array Operations Site (AOS)
– Antennas + Receivers + Correlator
2. Operations Support Facility (OSF)
– Quality Assurance Level 0 (“QA0”)
3. Santiago Central Offices (SCO)
– Quality Assurance Level 1 (“QA1”)
4. ALMA Regional Center (ARC)
– Quality Assurance Level 2 (“QA2”)
5. User (YOU)

## Slide 13: ALMA Level One Science Goals
The ability to detect spectral line emission from CO or C+ in a normal galaxy like the Milky Way at a redshift of z = 3, in less than 24 hours of observation.
The ability to image the gas kinematics in a solar-mass protostellar/ protoplanetary disk at a distance of 150 pc (roughly, the distance of the star-forming clouds in Ophiuchus or Corona Australis), enabling one to study the physical, chemical, and magnetic field structure of the disk and to detect the tidal gaps created by planets undergoing formation.
The ability to provide precise images at an angular resolution of 0.1″. Here the term "precise image" means an accurate representation of the sky brightness at all points where the brightness is greater than 0.1% of the peak image brightness. This requirement applies to all sources visible to ALMA that transit at an elevation greater than 20 degrees.

## Slide 14: Some cool ALMA images
ALMA image of a z=8.38 galaxy
Protoplanetary disks
Notes: Galaxy rich in dust based on imaged of lensed 600 million year old galaxy Abell 2744_YD4.
Bottom left disk is L1448 IRS3B, with a second star forming in a fragmented disk

## Slide 15
Remotely operated from
OSF Control room
An array of 66 antennas,
using aperture synthesis as a “zoom lens”
over the entire accessible mm/submm wavelength range up to 1 THz
ALMA
At 5000m
compact
Extended – up to 15 km
Built to operate
>30 years
Notes: If you’re here at this splinter session, I imagine I don’t need to tell you this, but ALMA is a mm/submm telescope accessible at frequencies up to a THz
Operates in a variety of configurations: compact for excellent recovery of low surface brightness emission,
particularly when combined with the Morita array (ACA, the 7m and total power antennas), and extended for very high resolution imaging, with many steps in between.
In fact, I’m sure most of you are aware of the recent observations of HL Tau, but I’d be remiss if I didn’t mention the most exciting image to come from our recent successful Long Baseline Campaign, the high resolution imaging of the proto-planetary disk around HL Tau…

## Slide 16: Basic Capabilities of ALMA
At least fifty 12-meter antennas for sensitive, high resolution imaging
Four additional 12-meter antennas, providing total power, and twelve 7-meter antennas comprising the ALMA Compact Array (ACA), enhancing the fidelity of wide field imaging
Imaging ability in all atmospheric windows from 3.6 mm to 0.3 mm (84 GHz to 950 GHz), with coverage down to 10 mm (30 GHz) possible through future receiver development
Array configurations with maximum baselines from approximately 150 meters to 15 km
Ability to image sources many arcminutes across at arcsecond resolution
Top spatial resolution of 5 milli-arcseconds (better than the VLA and HST)
Top velocity resolution better than 0.05 km/s

## Slide 17: ALMA in a Nutshell...
Angular resolution down to 0.015” (at 300 GHz)
Sensitive, precision imaging 84 to 950 GHz (3 mm to 315 µm)
State-of-the-art low-noise, wide-band receivers (8 GHz bandwidth)
Flexible correlator with high spectral resolution at wide bandwidth
Full polarization capabilities
Estimated 1 TB/day data rate
All science data archived
Pipeline processing
17
ALMA is10-100 times more sensitive and has 10-100 times better angular resolution than the previous generation of mm interferometers
ALMA is a telescope for all astronomers

## Slide 18
ALMA Long Baseline Campaign
CARMA Observation of HL Tau, resolution of ~25AU
Notes: Young Star ~1 Million Years, one of the nearest star forming regions to Earth (~450 light yr)
The best image of HL Tau previously is from CARMA with a resolution of ~25AU… the power of ALMA in its extended configuration is apparent here with a resolution of 5 AU
Able to see several gaps in the disk almost certainly reflect young planets, which is “disturbing” to planet formation theories
Going by the number of hits, the press release of HL Tau image was seen by almost 10% of the Earth’s population
But go and hear Al’s talk for more details on the science.

## Slide 19: ALMA Current Status
Construction Project ended in September 2014
Routine science observing now extends to the full 15 km baselines
All 66 antennas accepted
  Currently 64 antennas are at the high site (AOS), of which ~47 on average (up to max ~54) are being used for Cycle 3-5 observations
  Some construction and verification items remain to be finished (e.g., Bands 4, 8, 10; various observing modes)
The ACA (Atacama Compact Array) or Morita-san Array – up to 12x7m antennas and 4x12m antennas for TP observations – has been accepted and has been used from Cycle 2 onward
Notes: LBC (and other commissioning campaigns) – come to Stuartt’s talk tonight at the town hall to hear more
The number of antennas included in Cycle 2 observations includes some combination of 2-3 TP, 8-10 7m antennas, and 37-41 12m elements
Construction + commissioning still being finished – in addition to observing at Bands 4, 8, 10:
spectral line polarization; OTF interferometry; mosaicking of ephemeris observations; routine solar obs

## Slide 20: ALMA Receivers: Current Status
Receiver bands currently installed on all antennas
  Band 3, 3mm (84-116 GHz)
  Band 4, 2mm (125-163 GHz)
  Band 6, 1mm (211-275 GHz)
  Band 7, 850 mm (275-370 GHz)
  Band 9, 450 mm (602-720 GHz)
  Band 8, 650 mm (385-500 GHz)
  Band 10, 350 mm (787-950 GHz)
  + Band 5 on some antennas
Notes: Again, Stuartt will discuss ongoing verifications of new capabilities tonight at the town hall

## Slide 21: Comparisons with other mm interferometers
SMA
CARMA
PdBI
NMA
ALMA
Number of baselines NB: N(N-1)/2 = 1225, much better instantaneous sampling of the uv plane, better overall image fidelity
NB (PdBI) = 45
NB (CARMA) = 253
NB (NMA) = 15
NB (SMA) = 27
NB (VLA) = 351
22,619 m2
7069 m2
3129 m2
1885 m2
905 m2
(VLA surface area of 53,014 m2 not shown)

## Slide 22
22
ALMA, Full Science
50(+12+4)
6
8
Collecting Area
~ sensitivity
Spectral Coverage
Cycle 3
36+ (+10+2)
Cycle 0
16(+0+0)
CARMA
23

## Slide 23: ALMA arrays: the 12-m Array
× 25
× 25
VertexRSI antennas:
“ DV## ”
AEM antennas:
“ DA## ”
Number: 50 × 12-m antennas
Composition: steel, CFRP, aluminum, and Invar
Weight: >100 tons
Max slew rate: 0.5° s-1
Pointing: <2” (absolute) all sky; <0.6” in 2° rad (offset)
Parabolic surface accuracies of <25 μm rms
Minimum 40 antennas available for Cycle 4
Notes: AEM = Alcatel Alenia Space European Industrial Engineering MT Aerospace

## Slide 24: ALMA arrays: the 12-m Array
12-m antennas are movable to various stations across the Chajnantor plateau
Specialized trans-porters (named “Otto” and “Lore”) are used to move antennas around (also return them to the OSF for maintenance visits)
“Lore”
Credit: ESO/P. Martinez

## Slide 25: ALMA arrays: the 12-m Array
Cycle 3 configurations: min baseline = 14.7 m, max baseline = 9.743 km
2 km
2 km
12 km
12 km
2 km
12 km
2 km
2 km
2 km
2 km
2 km
12 km
C36-1
C36-2
C36-3
C36-4
C36-5
C36-6
C36-7
C36-8
“summer”
“winter”

## Slide 26: Configurations

## Slide 27: ALMA arrays: the ALMA Compact Array (ACA)
Number: 12 × 7-m antennas
Antennas are fixed in position
Min / Max baselines: 8.7 m / 32 m
Surface accuracy: <20 μm rms
Used for low spatial frequency data
MELCO antennas:
“ PM## ”
Minimum 10 antennas available for Cycle 4
Random Swede
Notes: ACA only intended to complement 12-m array observations…for now.

## Slide 28: ALMA arrays: the Total Power “Array” (TPA)
Number: 4 × 12-m antennas
Antennas are also fixed in position
Nutating secondaries available for sky subtraction
Signals not necessarily correlated but signals can be combined with those from the ACA if needed
Used to obtain zero-spacing spatial frequency data by acting as single-dish telescopes that observe simultaneously
MELCO antennas:
“ CM## ”
Minimum 3 antennas available for Cycle 4

## Slide 29: Trade offs of resolution and MRS

## Slide 30: Receiver Bands
ALMA will have receivers over all submm bands
1
2
4
5
8
10
transparent
opaque
longer wavelength
shorter wavelength
9 mm
350 mm
submillimetre wavelengths
1
2
4
5

## Slide 31: Receiver Bands + Sensitivities
Also “in the works”:
- Band 1: 35-52 GHz
- Band 2: 67-90 GHz
- Band 5: 163-211 GHz
- Band 11? : 1.0-1.6 THz
Continuum sensitivities estimated from a total of 7.5 GHz dual polarization band width in 60 seconds

## Slide 32: Receiver Bands
Band 3 receiver
cartridges
Cryostat
(exterior)
Cryostat
(interior)

## Slide 33: Correlators: the 64-input Correlator
A state-of-the-art FXF “correlator” (signal combiner) with 134 million processors capable of performing 17 quadrillion operations per second  produces “visibilities”
Correlator Exterior (ALMA)
Digital Filter Circuit Boards (ALMA)
Notes: FXF – Filtering, correlation, and Fourier transform

## Slide 34: Correlators: the 64-input Correlator
Up to 4 basebands can be placed with a given receiver band (with restrictions)
Time Division Mode (TDM): low spectral resolution (continuum) data at a low data rate; fast operations; ~1.875 GHz per baseband
Frequency Division Mode (FDM): higher spectral resolutions (lines); higher data rates; smaller band widths per baseband; 1, 2, or 4 spectral windows per baseband possible
1875
(due to filtering)
ALMA Baseband Options (Cycle 5)

## Slide 35: Correlators: the 64-input Correlator
Actual spectral resolution is 2× channel spacing due to the correlator performing Hanning smoothing on the data
Single pol’n modes also available, yield double the channel number and half the channel spacing
4 x “2 GHz” basebands = 8 GHz dual-pol band width
More baseband options to be commissioned later
1875
(due to filtering)
ALMA Baseband Options (Cycle 5)

## Slide 36
Output of interferometric observation is in the form of a “cube” of data – the third dimension is frequency.
Notes: So weve been talking a lot about the 2d image, With ALMA, you can make a 2D image (a continuum image). Sometimes you are only interested in an image in the x,y plane, and you can average all of these channels together to get a 2 dimensional image. Other times you are only interested in a spectrum, to determine molecular abundances in a region, for example, so you can integrate over an area in the x,y plane, and just plot the intensity as a function of frequency. But you always have the option to do both, or to keep the whole cube, after the observations are made.

## Slide 37: Correlators: the ACA Correlator
The ACA (and TPA) have an separate correlator that can have up to 16 inputs
Can run simultaneously with the 12-m Array + 64-input correlator
An “FX” design, different architecture from 64-input correlator
Same baseband modes and spectral window options as 64-input correlator
Two quadrants of ACA Correlator
c. ALMA/S. Okumura

## Slide 38: Other ALMA Capabilities
What is ALMA?
38
Some of these are now offered, but note some are considered “non-standard” and access just 20% of the available time:
High dynamic range imaging
Multi-band observations
Multiple spectral window observations
Polarization
TPA+ACA+12-m Array combination
Capabilities are improving with time and continued effort!

## Slide 39: The ALMA Proposal Preparation Process
How to get started and what to expect

## Slide 40
Proposal Checklist
Read relevant documentation (CfP Guide, Primer, etc.)
Create an ALMA account by registering at the Science Portal (almascience.org)
Download the Observing Tool (OT) & related guides
Prepare the Science Case
Prepare Science Goals (sources, frequency & correlator setup, integration times) within the OT
Make use of the Helpdesk & the Knowledgebase

## Slide 41
Cycle 6 Documentation & Timeline
Call for Proposals
Proposer’s Guide
ALMA Primer
OT Guide
ALMA Tech Handbook
Timeline for Cycle 6
  Mar. 21 – Call for Proposals
  Apr. 19 – Proposal Deadline
  Aug 2018 – Results to PIs
  Sept 2018 – PIs submit SBs
  Oct. 2018 – Start of Cycle 6
  Duration – 11-12 months

## Slide 42
ALMA Science Portal @ NRAO
www.almascience.org
Notes: Call for Proposals, Helpdesk, NRAO User Support, and Account access.

## Slide 43: Downloading the ALMA OT
Java 9

## Slide 45
Must include:
  Astronomical Importance
  Estimated intensity, S/N
May include:
  Figures
  Tables
  References
Free-form PDF document
  12+ font, English only
  20 MB file size
  4 pages (6 for Large Projects)
Science Case
Notes: Check what LST ranges are available for what configurations!
From the Proposer’s Guide: “Additionally, [the science case] should explain how the expected intensity of the target source(s) was estimated and justify the Signal-to-Noise (S/N) ratio required to achieve the scientific objectives of the project as well as, when appropriate, the size of the target sample.”

## Slide 46: Different bands require very different conditions

## Slide 47
Histograms of the anticipated amount of observing time available versus LST for the antenna configurations in Cycle 5. Also shown are histograms of the time available for Large Programs, as well as high frequency observations (Bands 8, 9, and 10) based on historical PWV data
ALMA Observing Strategies (Cycle 5)

## Slide 48: Helpful Tools
Sensitivity Calculator:
Enter in declination, angular resolution, band width, desired sensitivities, etc. to see how long your project will take with the 12-m Array, the ACA, and the TPA
No overheads are taken into account
Even though you do not request a set “time” with ALMA, having a sense of how much time you are requesting is a good idea

## Slide 49: Splatalogue
www.splatalogue.net

## Slide 50: Using the OT

## Slide 55
When possible, use the spectral averaging options.
Most people try this only when confronted with a data rate that sets off a flag
In practice, this will help you immensely; the data rate and data volume will be reduced
Final data set will be smaller and easier to deal with.

## Slide 59
Spectral resolution selected to achieve velocity resolution across a line; ensure the rms PER CHANNEL is deep enough for your science, not the entire bandwidth

## Slide 60
Click here to make sure that your project can be validated by the OT. If it won’t, you will not be able to submit it.
When you are satisfied that your proposal is complete, click here to submit your project to the ALMA Archive

## Slide 61: Observing Strategy
Choose your array by largest angular scale of target
  Interferometers act as spatial filters - shorter baselines are sensitive to larger targets, so remember:
    Spatial scales larger than the smallest baseline cannot be imaged
    Spatial scales smaller than the largest baseline cannot be resolved
Calibration Requirements (Handled by ALMA):
  Gain calibrator: solves for atmospheric and instrumental variations with time.
    Usually a bright quasar near science target
  Bandpass calibrator: fixes instrumental effects and variations vs frequency
    Usually a bright quasar
  Absolute flux calibrator: used to scale relative amplitudes to absolute value
    Usually a solar system object or quasar
Notes: As far as calibrators go, note that to plan observations, you don’t need to pick these! ALMA does it for you!

## Slide 62: Calibration Process
Calibration is the effort to measure and remove the time-dependent and frequency-dependent atmospheric and instrumental variations.
Steps in calibrating interferometric data:
(Note: You don’t have to worry about these in your observational set up!)
Bandpass calibration (correct frequency-dependent telescope response)
Phase and amplitude gain calibration (remove effects of atmospheric water vapor and correct time-varying phases/amplitudes)
Set absolute flux scale
Notes: Also point/focus/delay calibration step and system temperature step and step for flagging bad data

## Slide 63: Bandpass Calibration: Phase
Baselines to one antenna
Antenna-based Bandpass Solutions
* Analogous to optical “flat fielding” + bias subtraction for each antenna.
* Primarily correcting for frequency dependent telescope response (i.e. in the correlator/spectral windows)
* Done once in an Scheduling Block, uses bright point sources like quasars
* Typically, baseline responses are inverted to antenna-based correction
Notes: Typically, baseline responses are inverted to antenna-based correction
Imperfections = channel to channel variation in the phase
Goal is to get flat spectra

## Slide 64: Bandpass Phase vs. Frequency (Before)

## Slide 65: Bandpass Phase vs. Frequency (After)

## Slide 66: Bandpass Calibration: Amplitude
Amplitude Before Bandpass Calibration
Baselines to one antenna
Bandpass solutions for individual antennas

## Slide 67: Atmospheric Phase Correction
Variations in the amount of precipitable water vapor cause phase fluctuations that result in:
  Low coherence (loss of sensitivity)
  Radio “seeing” of 1arcsec at 1mm
  Anomalous pointing offsets
  Anomalous delay offsets
Patches of air with different water vapor content (and hence index of refraction) affect the incoming wave front differently.

## Slide 68: Phase & Amplitude Gain Calibration
Determines the variations of phase and amplitude over time
First pass is atmospheric correction from Water Vapor Radiometers readings
Final correction from gain calibrator (point source near to target) that is observed every few minutes throughout the observation (analogous to repeat trips to a standard star)

## Slide 69: Water Vapor Correction on ALMA
Phase vs. Time
One 600m Baseline
~600 GHz
Before WVR, After WVR

## Slide 70: Phase Calibration
The phase calibrator must be a point source close to the science target and must be observed frequently. This provides a model of atmospheric phase change along the line of sight to the science target that can be compensated for in the data.
Time
Phase
Corrected using point source model
Notes: Assume phase calibrator is a quasar which has zero phase and constant amplitude

## Slide 71: Flux (or Amplitude) Calibration
Two Steps:
1. Use calibration devices with known temperatures (hotload and ambient load) to measure System Temperature frequently.
2. Use a source of known flux to convert the signal measured at the antenna to common unit (Janskys). If the source is resolved, or has spectral lines, it must be modeled very well.
The derived amplitude vs. time corrections for the flux calibrator are then applied to the science target.
Notes: These are somewhat analagous to standard stars in the optical

## Slide 72: Amp-Calibrators Amp vs. uv-distance (Before)

## Slide 73: Amp-Calibrators Amp vs. uv-distance (Model)

## Slide 74: Amp-Calibrators Amp vs. uv-distance (After)

## Slide 75: Simulating ALMA data
You may want to determine if an idea you have for ALMA is feasible, or refine the observations with a simulation
  Can show the impact of using different configurations
  Different bands
  Varying integration times

## Slide 76: Trade offs of resolution and MRS

## Slide 85: Simulating ALMA data in CASA
See CASAguides
For more info on
Simulating ALMA data
Simobserve output
Simanalyze output
Example of an M51-like galaxy observed at z=0.1

## Slide 86
almascience.org
is the place to go for additional ALMA information
Assignment help: Brenda.Matthews@nrc-cnrc.gc.ca