## Slide 1: Interferometry and ALMA Part 1
Brenda Matthews
NRC Herzberg
North American ALMA Regional Center – Victoria
(thanks to J. Di Francesco, S. Dougherty, C. Chandler, D. Wilner & C. Brogan)

## Slide 2: Radio Astronomy
Now used to refer to most telescopes using heterodyne technology
Notes: Radio astronomy used to be defined with a rough wavelength cut where we have a block of atmospheric transmission and ground-based observations are possible but now this def has expanded.
Still have Earth's ionosphere bounding ground-based obs below nu ~ 10 MHz (lambda ~ 30 m) but it’s about the technology

## Slide 3: What is heterodyne?
In a heterodyne receiver, observed sky frequencies are converted to lower frequency signals by mixing with a signal artificially created by a Local Oscillator. The output can then be amplified and analyzed more easily while retaining the original phase and amplitude information.
Image from Alessandro Navarrini (IRAM)
Notes: New definition of radio is something that uses heterodyne technology. The process varies slightly at diff wavelengths within the radio regime, but the important step is that observed sky frequencies are mixed with an LO to produce a lower frequency signal (they are down converted) so that they can be analyzed more easily
Down converting helps because: 1) receiver only has to work at IF output frequency; 2) I think low freq signals are easier to analyze because of how noise works? They have higher snr?

## Slide 4: Long wavelength means no glass mirrors
Notes: The imperfections in your dish can be relative to the wavelengths you are observing. No more pristine glass mirrors! At arecibo you need special shoes even
On the bottom: LWA in New Mexico (decameter array i.e. 10 meters)

## Slide 5: What can we observe? (MHz-GHz range)
Relic emission from old radio galaxies
Jupiter’s radiation belt at 100MHz
Synchrotron emission from extended radio galaxies (5 GHz)
Images from NRAO Image Gallery: http://images.nrao.edu/
Notes: Synchrotron from Jupiter radiation belt
Nonthermal so doesn’t depend on temperature of source, just need electrons spiraling around a magnetic field

## Slide 6: What should we observe?
At low frequencies (MHz-GHz):
HI emission and absorption, free-free absorption in galaxies
H2O, OH or SiO masers in galaxies and stars
Images from NRAO Image Gallery
http://images.nrao.edu/
Notes: SiO masers in TX Cam (Diamond & Kemball) Masers are very cool. These are like lasers, but at microwave frequencies (hence the name), and they occur in space. So when you have a region that has molecular gas, and enough energy is being dumped into it, either radiatively or collisionally, you can get population inversion which will amplify any ambient emission
Watching the atmosphere of the Mira variable star via SiO masers as star fluctuates

## Slide 7: At higher frequencies we can observe a broad range of molecular lines
What can we observe?
Images from ALMA Science Verification (Brogan)
Notes: We saw this galaxy pair, the Antennae, in one of the labs. These galaxies are in the process of colliding, and as a result there are regions where dense carbon monoxide gas traces very high rates of star formation

## Slide 8: Why do we need interferometers?
Angular resolution for most telescopes is ~ λ/D
  D is the diameter of the telescope
  λ is wavelength of observation
For example, Hubble Space Telescope:
  λ ~ 1um / D of 2.4m = resolution ~ 0.13”
To reach that resolution for a λ ~1mm observation, one would need a 2 km-diameter dish!
Instead, we use arrays of smaller dishes to achieve the same high angular resolution at radio frequencies
This is interferometry
Notes: What kind of resolutions can we get at radio wavelengths?
So we can build larger telescopes or go to smaller wavelengths
In a way like using a giant mirror which is very dirty. The only places that it’s reflective are where you have antennas on the ground.

## Slide 9: What is an interferometer?
9
An interferometer measures the interference pattern produced by multiple apertures, much like a 2-slit experiment.
*However, the interference patterns measured by radio telescopes are produced by multiplying - not adding - the wave signals measured at the different telescopes (i.e. apertures)
Notes: You may recall the double slit experiment from your first year physics classes, but in case you’re like me and that was a long time ago ...

## Slide 10: How do we use interferometry?
A signal from space arrives at each antenna at a slightly different time (due to different travel lengths) depending on the location of the antenna in the array.
The signals arriving from slightly different points in the sky arrive at slightly different times at each antenna. This provides location information within the telescope beam and thus positional information about the emitting object.
The signal from each antenna is then combined with every other antenna in a correlator, where the time delay is measured and compensated for in the software.

## Slide 11: Some instrument details…
To precisely measure arrival times we need very accurate clocks
At Band 10 one wavelength error = 1 picosecond (!!)
We need << 1 wavelength timing precision so each antenna has an on-board clock with high sampling rates
Once determined, the reference time is distributed to all antennas
Correlator
Reference
Notes: Emphasize what a pico is 10^-12 !!!
Signals going out to the antennas involved control software for pointing and tracking sources, for tuning the receivers, for timing reference, for additional commands such as putting the hotload in the beam to measure the system temperature or to update the subreflector position. Signals coming back from the antennas involve device health, fiber polarization to check the fiber length, the astronomical signal that’s going into the correlator

## Slide 12: Some instrument details…
Signal from each antenna are digitized and sent to the correlator for multiplication & averaging.
For ~50 antennas the data rate is 600 GB/sec for the correlator to process
Correlator
Reference
Notes: 8 windows * 4Gsps * 3bits = 12GB per second from each antenna = 600 GB/sec for correlator to process

## Slide 13
Interferometry: Spatial Scales
The field of view is given by the beam of a single antenna (corresponding to the resolution for a single dish telescope or the primary beam)
The resolution is given by the largest distance between antennas (called the synthesized beam)
The maximum recoverable scale that can be imaged is given by the shortest distance between antennas
Notes: Note the incomplete filling of the uv plane. Central hole means missing total flux

## Slide 14: Characteristic Angular Scales: M100
12m data reveals information on smaller spatial scales (denser, clumpier emission)
7m data reveals information on larger spatial scales (diffuse, extended emission)
To get both: you need a combined image
Notes: Let’s have a look at what this looks like (all moment 0 maps of grand design spiral in Virgo)
We’ll discuss later that there is a way to enter in your desired resolution and your LAS and the OT will tell you if you need additional 7m data

## Slide 15: The Plan
Introduction  James
Basics of Radio Astronomy  James
Basics of Aperture Synthesis
Imaging
Deconvolution
An example ALMA data reduction exercise (25%)
Specifics about ALMA (next week)
Thompson, A.R., Moran, J.M. & Swensen, G.W. 1986, “Interferometry and Synthesis in Radio Astronomy” (New York: Wiley); also 2nd edition

## Slide 16: Aperture Synthesis

## Slide 17
Signals at each point in the aperture are brought together in phase at the antenna output (the focus)
Imagine the aperture to be subdivided into N smaller elementary areas; the voltage, V(t), at the output is the sum of the contributions ΔVi(t) from the N individual aperture elements:
Aperture Synthesis
Output of a Filled Aperture
∑ΔVi(t)

## Slide 18
Single dish: diameter is responsible for sensitivity, field of view, resolution
Interferometer: takes this apart

## Slide 19
Longest Distance for resolution, synthesized beam
Single dish: diameter is responsible for sensitivity, field of view, resolution
Interferometer: takes this apart

## Slide 20
Longest Distance for resolution, synthesized beam
Single dish: diameter is responsible for sensitivity, field of view, resolution
Interferometer: takes this apart
Diameter of Single element: Field of View, primary beam

## Slide 21
Longest Distance for resolution, synthesized beam
Number of dish apertures:
sensitivity
Single dish: diameter is responsible for sensitivity, field of view, resolution
Interferometer: takes this apart
Diameter of Single element: Field of View, primary beam

## Slide 22
The radio power measured by a receiver attached to the telescope is proportional to a running time average of the square of the output voltage:
Any measurement with the large filled-aperture telescope can be written as a sum, in which each term depends on contributions from only two of the N aperture elements
Each term áDViDVkñ can be measured with two small antennas, if we place them at locations i and k and measure the average product of their output voltages with a correlation (multiplying) receiver
Aperture Synthesis
Aperture Synthesis: Basic Concept
Autocorrelation term, sky + source
Notes: Interferometers keep only the second term; first term not used; it’s the total flux of the sky + source, so we can’t just use the autocorrelation b/c it is both dominated by sky though largely resolved out

## Slide 23
If the source emission is unchanging, there is no need to measure all the pairs at one time
One could imagine sequentially combining pairs of signals. For N sub-apertures there will be N(N-1)/2 pairs to combine
Adding together all the terms effectively “synthesizes” one measurement taken with a large filled-aperture telescope
Can synthesize apertures much larger than can be constructed as a filled aperture, giving very good spatial resolution
Aperture Synthesis
Aperture Synthesis: Basic Concept

## Slide 24
What is the interferometer response as a function of sky position, l = sin α ?
In direction s0 (a = 0) the wavefront arriving at telescope #1 has an extra path b sinq to travel relative to #2
The time taken to traverse this extra path is the geometric delay, tg = b sinq / c
This delay is compensated for by inserting a signal path delay for #2 equivalent to tg
Aperture Synthesis
A Simple 2-Element Interferometer

## Slide 25
At angle a, a wavefront has an extra path x = u sina = ul to travel
Expand to 2D by introducing b orthogonal to a, m = sinb, and v orthogonal to u, so that in this direction the extra path y = vm
Write all distances in units of wavelength, x º x/l, y º y/l, etc., so that x and y are now numbers of cycles
Extra path is now ul + vm
V2 = V1 e-2πi(ul+vm)
Aperture Synthesis
Response of a 2-Element Interferometer
Notes: This extra path in the phase on the 2D sky we call a visibility. It’s value is inherently linked to both the offset from the pointing centre of the telescopes through x and y and to the separation of the telescopes on the ground through u and v.

## Slide 26
The output from the correlator (the multiplying and time-averaging device) is:
For (l1≠l2, m1≠m2) the above average is zero (assuming mutual sky), so
Aperture Synthesis
Correlator Output

## Slide 27
Thus, the interferometer measures the complex visibility, V(u,v), of a source, which is the FT of its intensity distribution on the sky, I(l,m):
  u,v are spatial frequencies in the E-W and N-S directions,
    a.k.a. the projected baseline lengths measured in units of wavelength, i.e., B/λ
  l, m are direction cosines relative to a reference position in the E-W and N-S directions
  (l = 0, m = 0) is known as the phase center
  the phase Φ contains information about the location of structure with spatial frequency u,v relative to the phase center
Aperture Synthesis
The Complex Visibility

## Slide 28
This FT relationship is the van Cittert-Zernike theorem, upon which synthesis imaging is based
It means there is an inverse FT relationship that enables us to recover I(l,m) from V(u,v):
The correlator measures both real and imaginary parts of the visibility to give the amplitude and phase:
A=|V |
f
Aperture Synthesis
The Complex Visibility

## Slide 29: Visibility and Sky Brightness
from the van Citttert-Zernike theorem (TMS Appendix 3.1)
  for small fields of view: the complex visibility,V(u,v) is the 2D Fourier transform of the brightness on the sky, T(x,y), or I(l,m)
  u,v (wavelengths) are spatial frequencies in E-W and N-W directions, i.e. the baseline lengths
  x,y (rad) are angles in tangent plane relative to a reference position in the E-W and N-S directions
T(x,y)
x
y

## Slide 30: Pause for questions
Once you are comfortable with the idea of the nomenclature of a visibility, the issue becomes how best to sample those visabilities to get the best realization of I(l,m) (or T(x,y))
The real intensity on the sky is measurable from V(u,v), but measurements cannot be made on all baselines or over all spatial frequencies

## Slide 31
Fourier theory states that any signal (including images) can be expressed as a sum of sinusoids
Jean Baptiste Joseph Fourier 1768-1830
signal
4 sinusoids
sum
Aperture Synthesis
The Fourier Transform
the Fourier Transform contains all information of the original
(x,y) plane and (u,v) plane are conjugate coordinate systems
  I(x,y) V(u,v) = FT{I(x,y)}

## Slide 32: The Fourier Transform
Fourier theory states that any signal (here images) can be expressed as a sum of sinusoids
(x,y) plane and (u,v) plane are conjugate
  T(x,y) V(u,v) = FT{T(x,y)}
in this example a single Fourier component encodes all
  the spatial frequency = period of the wave
  the magnitude = contrast
  the phase (not shown) = shift of wave with respect to origin
Fourier Transform image contains all information of original image

## Slide 33
complex numbers: (real, imaginary) or (amplitude, phase)
  amplitude tells “how much” of a certain spatial frequency component
  phase tells “where” this component is located
I(x,y)
Amp{V(u,v)}
Pha{V(u,v)}
Aperture Synthesis
Amplitude and Phase

## Slide 34
complex numbers: (real, imaginary) or (amplitude, phase)
  amplitude tells “how much” of a certain spatial frequency component
  phase tells “where” this component is located
I(x,y)
Amp{V(u,v)}
Pha{V(u,v)}
Aperture Synthesis
Amplitude and Phase

## Slide 35
I(x,y)
narrow features transform to wide features (and vice-versa)
Amp{V(u,v)}
Gaussian
 Function
Constant
Gaussian
Aperture Synthesis
Some 2-D Fourier Transform Pairs

## Slide 36
elliptical
Gaussian
sharp edges result in many high spatial frequencies
elliptical
Gaussian
Disk
Bessel
Aperture Synthesis
More 2-D Fourier Transform Pairs
I(x,y)
Amp{V(u,v)}

## Slide 37
The FT of a single visibility measurement is a sinusoid with spacing 1/u = l/B between successive peaks, or “fringes”
Build up an image of the sky by summing many such sinusoids (addition theorem)
FT scaling theorem shows:
  Short baselines have large
  fringe spacings and measure
  large-scale structure on the sky
  Long baselines have small
  fringe spacings and measure
  small-scale structure on the sky
- + - + - + - Fringe Sign
l/B rad.
Source
brightness
Aperture Synthesis
Picturing the Visibility: Fringes
Notes: Projection of screen onto the sky to give the idea of what do you measure; they are interfered voltages (interferometric beam response is like a filter over the emission at that position on the sky (voltage)

## Slide 38: Visibility and Sky Brightness

## Slide 39: Visibility and Sky Brightness

## Slide 40: 2D Fourier Transform Pairs
T(x,y) Amp{V(u,v)}
structure on many scales
T(x,y) is real, but V(u,v) is complex (in general)
  Real and Imaginary
  Amplitude and Phase
  Amplitude tells “how much” of a certain frequency component, Phase tells “where”
  V(-u,-v) = V*(u,v) where * is complex conjugation (Hermitian)
V(u=0,v=0)  integral of T(x,y)dxdy = total flux

## Slide 41
sample V(u,v) at enough points to synthesize the equivalent large aperture of size (umax,vmax)
  1 pair of telescopes  1 (u,v) sample at a time
  N telescopes  number of samples = N(N-1)/2
  fill in (u,v) plane by making use of Earth rotation:
    Sir Martin Ryle, 1974 Nobel Prize in Physics
  reconfigure physical layout of N telescopes for more
2 configurations
of 8 SMA antennas
345 GHz
Dec = -24 deg
Sir Martin Ryle 1918-1984
Aperture Synthesis
Aperture Synthesis
“uv coverage” in the “uv plane”

## Slide 42: Aperture Synthesis Telescopes
(e)VLA
ATCA
IRAM PdBI / NOEMA
SMA
ALMA

## Slide 43: Imaging

## Slide 44
in aperture synthesis, V(u,v) samples are limited by number of telescopes, and Earth-sky geometry
  high spatial frequencies:
    maximum angular resolution
  low spatial frequencies:
    extended structures invisible
    (NB. There is a maximum scale that can be imaged; also ``zero-spacing problem” = no large scales)
  irregular within high/low limits:
    sampling theorem violated
    still more information missing
Imaging
(u,v) Plane Sampling in practice

## Slide 45
Sampling Function
Each antenna pair samples only one spot; the array cannot sample the entire Fourier/uv domain resulting in an imperfect image
Small uv-distance: short baselines (measure extended emission)
Long uv-distance: long baselines (measure small scale emission)
Orientation of baseline also determines orientation in the uv-plane
Notes: Note the incomplete filling of the uv plane. Central hole means missing total flux

## Slide 46
uv coverage: why the central hole?
The central hole in the sampling of the uv plane arises due to a limitation on the shortest baselines
The largest angular scale that an interferometer is sensitive to is given by the shortest distance between 2 antennas.
A single antenna diameter will always be < the shortest distance between two antennas.
So the field of view is always > the largest angular scale
If your source is extended, you will always have some flux at short spacings (i.e. extended emission) that is not recovered.
Solutions: We can extrapolate to these shorter spacings after our observations are taken or we can fill in the information with 7m observations or ultimately single dish data.
Notes: Note the incomplete filling of the uv plane. Central hole means missing total flux

## Slide 47
sample Fourier domain at discrete points, i.e.,
so, the inverse Fourier transform of the ensemble of visibilities is:
but the convolution theorem tells us:
where (the point spread function)
Fourier transform of sampled visibilities yields the true sky brightness convolved with the point spread function
(i.e., the “dirty image” is the true sky brightness convolved with the “dirty beam”)
Formal Description
I
I
I
Imaging
dij(u,v)
This is the “synthesized beam”

## Slide 48
uv plane analysis
  best for “simple” sources, e.g., point sources, disks
image plane analysis
  Fourier transform V(u,v) samples to image plane, get ID(x,y)
  but difficult to do science on dirty image
  deconvolve b(x,y) from ID(x,y) to determine (model of) I(x,y)
visibilities dirty image sky brightness
deconvolve
Fourier transform
How to analyze interferometer data?
Imaging

## Slide 49
B(u,v)
ID(x,y)
(dirty
image)
b(x,y)
(dirty
beam)
I(x,y)
Dirty Beam and Dirty Image
Imaging

## Slide 50: Details of the Dirty Image
Fourier Transform
  Fast Fourier Transform (FFT) much faster than simple Fourier summation, O(NlogN) for 2N x 2N image
  FFT requires data on regularly spaced grid
  aperture synthesis observations not on a regular grid…
“Gridding” is used to resample V(u,v) for FFT
  customary to use a convolution technique
    visibilities are noisy samples of a smooth function
    nearby visibilities not independent
  use special (“Spheroidal”) functions with nice properties
    fall off quickly in (u,v) plane (not too much smoothing)
    fall off quickly in image plane (avoid aliasing)

## Slide 51: Pixel Size and Image Size
pixel size
  should satisfy sampling theorem for the longest baselines, x < 1/2 umax , y < 1/2 vmax
  in practice, 3 to 5 pixels across the main lobe of the dirty beam (to aid deconvolution)
image size
  natural resolution in (u,v) plane samples FT{A(x,y)}, implies image size 2x primary beam
  if there are bright sources in the sidelobes of A(x,y), then they will be aliased into the image (need to make a larger image)

## Slide 52: Characteristic Angular Scales
Angular resolution of telescope array:
  ~ λ/Bmax , where Bmax is the longest baseline
Maximum recoverable scale:
  a source is resolved if the angular size > λ/Bmin
    (Bmin is the minimum separation between apertures)
Field of view of a single aperture (single dish):
  ~ λ/D, where D is the diameter of the telescope.
  If sources are more extended than the FOV, it can be observed using multiple pointing centers in a mosaic.
An interferometer is sensitive to a range of angular sizes
λ/Bmax < θ < λ/Bmin
Since Bmin> D, an interferometer is not sensitive to the large angular scales and cannot recover the total flux of resolved sources
Notes: At other wavelengths or with single dishes/mirrors we are used to thinking about resolution. But with interferometry we also have to think about LAS. This is bad because it means that if you have a star-forming region, for example, with hot cores and diffuse gas in between, you don’t gain any information about the diffuse gas. You just don’t detect it, it’s resolved out. On the other hand, this is good because we don’t need to worry about sky brightness on large scales, or atmospheric effects very much, you simply don’t see them. This is called spatial filtering.

## Slide 53
~4’
Band 3 (54”)
Band 6 (27”)
Band 9 (9”)
Band 7 (18”)
FOV [12 m]
B68 ALMA single pointing
Field of View: Single Pointing

## Slide 54
~4’
Nyquist Spacing
= 3-1/2 (/D) rad.
= 29.75” x
(/100 GHz)-1
= constant rms over inner area
Mosaics of up to 150 pointings OK
B68 ALMA Band 3 mosaic
Field of View: Mosaics

## Slide 55: Advantages of many antennas
Don’t need multiple reconfigurations to observe all objects
More sensitive (can do time variable)
How many antennas?
  Driven by sensitivity and imaging requirements
  Particularly dynamic range

## Slide 56
2 Antennas
Dirty Beam Shape and N Antennas
Imaging

## Slide 57
3 Antennas
Dirty Beam Shape and N Antennas
Imaging

## Slide 58
4 Antennas
Dirty Beam Shape and N Antennas
Imaging

## Slide 59
5 Antennas
Dirty Beam Shape and N Antennas
Imaging

## Slide 60
6 Antennas
Dirty Beam Shape and N Antennas
Imaging

## Slide 61
7 Antennas
Dirty Beam Shape and N Antennas
Imaging

## Slide 62
8 Antennas
Dirty Beam Shape and N Antennas
Imaging

## Slide 63
8 Antennas x 6 Samples
Dirty Beam Shape and N Antennas
Imaging

## Slide 64
8 Antennas x 30 Samples
Dirty Beam Shape and N Antennas
Imaging

## Slide 65
8 Antennas x 60 Samples
Dirty Beam Shape and N Antennas
Imaging

## Slide 66
8 Antennas x 120 Samples
Dirty Beam Shape and N Antennas
Imaging

## Slide 67
8 Antennas x 240 Samples
Dirty Beam Shape and N Antennas
Imaging

## Slide 68
8 Antennas x 480 Samples
Dirty Beam Shape and N Antennas
Imaging
Notes: Easy to see why early interferometric observations were called “tracks”, and you often needed several of them to actually achieve decent uv coverage and S/N.

## Slide 69: 32 Antennas – Instantaneous
Notes: With alma you have 50 antennas so n(n-1)/2 = 1225 pairs (and twice as many points on the uv plane) So you can add more visibilities by adding more antennas or …

## Slide 70: 32 Antennas – 8 hours
Notes: Here we fill in more uv coverage by letting the earth rotate (i.e. letting time pass) rather than adding more antennas
How much you filli n your uv plane (how well sampled it is) determines your image quality

## Slide 71: Dirty Beam Shape and Weighting
introduce weighting function W(u,v)
  W modifies sidelobes of dirty beam
  W is also gridded for FFT
“Natural” weighting
  W(u,v) = 1/2(u,v) at points with data and zero elsewhere where 2(u,v) is the noise variance of the (u,v) sample
  maximizes point source sensitivity (lowest rms in image)
  gives more weight to shorter baselines (larger spatial scales), degrades resolution

## Slide 72: Dirty Beam Shape and Weighting
“Uniform” weighting
  W(u,v) is inversely proportional to local density of (u,v) points, so sum of weights in a (u,v) cell is a constant (or zero)
  fills (u,v) plane more uniformly, so (outer) sidelobes are lower
  gives more weight to long baselines and therefore higher angular resolution
  degrades point source sensitivity (higher rms in image)
  can be trouble with sparse sampling (cells with few data points have same weight as cells with many data points)

## Slide 73: Dirty Beam Shape and Weighting
“Robust” (Briggs) weighting
  variant of “uniform” that avoids giving too much weight to cell with low natural weight
  implementations differ, e.g. SN is natural weight of a cell, St is a threshold
  large threshold natural weighting
  small threshold  uniform weighting
  parameter allows continuous variation between optimal angular resolution and optimal point source sensitivity

## Slide 74: Dirty Beam Shape and Weighting
“Tapering”
  apodize the (u,v) sampling by a Gaussian
  t = tapering parameter (in k; arcsec)
  like smoothing in the image plane (convolution by a Gaussian)
  gives more weight to shorter baselines, degrades angular resolution
  degrades point source sensitivity but can improve sensitivity to extended structure
  could use an elliptical Gaussian
  limits to usefulness

## Slide 75: Weighting and Tapering: Noise
Natural
+ Taper
4.2x3.9
=1.54
Robust
+ Taper
1.7x1.4
=1.30
Natural
1.7x1.4
=1.0
Uniform
0.9x0.7
=1.58
Robust
1.0x0.8
=1.28

## Slide 76: Weighting and Tapering: Summary
imaging parameters provide a lot of freedom
The corollary of this is that there is no “one right answer”  some people find this troubling!
 | Robust/Uniform | Natural | Taper
Resolution | high | medium | low
Sidelobes | lower | higher | depends
Point Source Sensitivity | lower | maximum | lower
Extended Source Sensitivity | lower | medium | higher

## Slide 77: Deconvolution

## Slide 78: Deconvolution
difficult to do science on dirty image, which is convolved with dirty beam
deconvolve b(x,y) from TD(x,y) to recover T(x,y)
information is missing, so be careful!
dirty image “CLEAN” image

## Slide 79: Deconvolution Philosophy
to keep you awake at night
   an infinite number of T(x,y) compatible with sampled V(u,v), i.e. “invisible” distributions R(x,y) where b(x,y)  R(x,y) = 0
    no data beyond umax,vmax  unresolved structure
    no data within umin,vmin  limit on largest size scale
    holes between umin,vmin and umax,vmax  sidelobes
  noise  undetected/corrupted structure in T(x,y)
  no unique prescription for extracting optimum estimate of true sky brightness from visibility data
deconvolution
  uses non-linear techniques effectively interpolate/extrapolate samples of V(u,v) into unsampled regions of the (u,v) plane
  aims to find a sensible model of T(x,y) compatible with data
  requires a priori assumptions about T(x,y)

## Slide 80: Deconvolution Algorithms
most common algorithms in radio astronomy
  CLEAN (Högbom 1974)  most common!
    a priori assumption: T(x,y) is a collection of point sources
    variants for computational efficiency, extended structure
  Maximum Entropy (Gull and Skilling 1983)
    a priori assumption: T(x,y) is smooth and positive
    vast literature about the deep meaning of entropy (Bayesian)
  hybrid approaches of these can be effective
deconvolution requires knowledge of beam shape and image noise properties (usually OK for aperture synthesis)
  atmospheric seeing can modify effective beam shape
  deconvolution process can modify image noise properties

## Slide 81: CLEAN in CASA
CLEAN is the imaging task in CASA. It:
takes the calibrated visibilities
grids them on the UV-plane
performs the FFT to a dirty image
deconvolves the image
restores the image from clean table and residual
corrects for the primary beam
Notes: 81
We’ll revisit imsize when we discuss mosaicing later

## Slide 82
The elements of an interferometer have finite size, and so have their own response to the radiation from the sky
This results in an additional factor, A(l,m), to be included in the expression for the correlator output, which is the primary beam or normalized reception pattern of the individual elements
Interferometer actually measures the FT of the sky multiplied by the primary beam response
Need to divide by A(l,m) to recover I(l,m), the last step of image production
Primary Beam FWHM is the “Field-of-View” of a single-pointing interferometric image
Aperture Synthesis
Correcting for the Primary Beam

## Slide 83: Basic CLEAN Algorithm
  Initialize
    a residual map to the dirty map
    a Clean component list to empty
  Identify strongest feature in residual map as a point source
  Add a fraction g (the loop gain) of this point source to the clean component list
  Subtract the fraction g times b(x,y) from residual map
  If stopping criteria not reached, go to step 2 (an interation)
  Convolve Clean component (cc) list by an estimate of the main lobe of the dirty beam (the “Clean beam”) and add residual map to make the final “restored” image
b(x,y)
TD(x,y)

## Slide 84: Basic CLEAN Algorithm (cont)
stopping criteria
  residual map max < multiple of rms (when noise limited)
  residual map max < fraction of dirty map max (dynamic range limited)
  max number of clean components reached
loop gain: good results for g ~ 0.1 to 0.3
easy to include a priori information about where to search for clean components (“clean boxes”)
  very useful but potentially dangerous!
Schwarz (1978): CLEAN is equivalent to a least squares fit of sinusoids (in the absense of noise)

## Slide 85: CLEAN
restored image
residual map
CLEAN model
TD(x,y)
Notes: 85

## Slide 86: CLEAN
restored image
residual map
CLEAN model
TD(x,y)

## Slide 87: CLEAN with Box
restored image
residual map
CLEAN model
TD(x,y)

## Slide 88: CLEAN with Poor Choice of Box
restored image
residual map
CLEAN model
TD(x,y)

## Slide 89: “Restored” Images
CLEAN beam size:
  natural choice is to fit the central peak of the dirty beam with elliptical Gaussian
  unit of deconvolved map is Jy per CLEAN beam area (= intensity, can convert to brightness temperature)
  minimize unit problems when adding dirty map residuals
  modest super resolution often OK, but be careful
“restored” image does not fit the visibility data
photometry should be done with caution
  CLEAN does not conserve flux (extrapolates)
  extended structure missed, attenuated, distorted
  phase errors (e.g. seeing) can spread signal around

## Slide 90: Noise in Images
point source sensitivity: straightforward
  telescope area, bandwidth, integration time, weighting
  in image, modify noise by primary beam response
extended source sensitivity: problematic
  not quite right to divide noise by n beams covered by source: smoothing = tapering, omitting data  lower limit
  always missing flux at some spatial scale
be careful with low signal-to-noise images
  if position known, 3 OK for point source detection
  if position unknown, then 5 required (flux biased by ~1)
  if < 6, cannot measure the source size (require ~3 difference between “long” and “short” baselines)
  spectral lines may have unknown position, velocity, width

## Slide 91
“dynamic range”
  ratio of peak brightness to rms noise in a region void of emission (common in astronomy)
  an easy to calculate lower limit to the error in brightness in a non-empty region
“fidelity”
  difference between any produced image and the correct image
  a convenient measure of how accurately it is possible to make an image that reproduces the brightness distribution on the sky
  need a priori knowledge of correct image to calculate
  fidelity image = input model / difference
  fidelity is the inverse of the relative error
Measures of Image Quality
Deconvolution

## Slide 92: CLEAN Variants
Clark CLEAN
  aims at faster speed for large images
  Högbom-like “minor” cycle w/ truncated dirty beam, subset of largest residuals
  in “major” cycle, cc’s are FFT’d and subtracted from the FFT of the residual image from the previous “major” cycle
Cotton-Schwab CLEAN (MX)
  in “major” cycle, cc’s are FFT’d and subtracted from ungridded visibilities
  more accurate but slower (gridding steps repeated)
Steer, Dewdny, Ito (SDI) CLEAN
  aims to supress CLEAN “stripes” in smooth, extended emission
  in “minor” cycles, any point in the residual map greater than a fraction (<1) of the maximum is taken as a cc
Multi-Resolution CLEAN
  aims to account for coupling between pixels by extended structure
  independently CLEAN a smooth map and a difference map, fewer cc’s

## Slide 93
Deconvolution algorithms : Hogbom
data visibilities
dirty image
model image
grid & FFT
Iterative removal of dirty beam
Subtracts full PSF in image domain
For complex images, errors can build

## Slide 94
Deconvolution algorithms : Clark
Subtracts truncated PSF in image domain
Periodically subtracts from gridded data in uv domain
minor cycle
data visibilities
gridded model
dirty image
model image
grid
Iterative removal of dirty beam
FFT
subtract
major cycle
gridded data
FFT

## Slide 95
Cotton-Schwab (csclean):
subtracts truncated PSF in image domain
major cycle subtracts from full visibilities
significant I/O per major cycle
Deconvolution algorithms: Cotton-Schwab
minor cycle
data visibilities
model visibilities
dirty image
model image
grid & FFT
Iterative removal of dirty beam
FFT & degrid
subtract
major cycle

## Slide 96: Maximum Entropy Algorithm
  Maximize a measure of smoothness (the entropy)
  subject to the constraints
  M is the “default image”
  fast (NlogN) non-linear optimization solver due to Cornwell and Evans (1983)
  optional: convolve with Gaussian beam and add residual map to make map
b(x,y)
TD(x,y)

## Slide 97: Maximum Entropy Algorithm (cont)
easy to include a priori information with default image
  flat default best only if nothing known (or nothing observed!)
straightforward to generalize 2 to combine different observations/telescopes and obtain optimal image
many measures of “entropy” available
  replace log with cosh  “emptiness” (does not enforce positivity)
less robust and harder to drive than CLEAN
works well on smooth, extended emission
trouble with point source sidelobes
no noise estimate possible from image

## Slide 98: Maximum Entropy
restored image
residual map
MAXEN model
TD(x,y)

## Slide 99: CLEAN details
Modes/Capabilities:
continuum: incl. multi-frequency synthesis (radial extent of each visibility due to bandwidth), and Taylor term expansion (to derive spectral index and curvature)
spectral line: data cubes (many planes) grids in velocity space, takes account of Doppler shift of line
mosaicking: combine multiple pointings to single image
w-projection/faceting for images beyond the half-power point
outlier fields to deconvolve strong sources in primary beam sidelobes
multiscale cleaning
Notes: 99
We’ll revisit imsize when we discuss mosaicing later

## Slide 100
CLEAN in CASA:

## Slide 101: Output of CLEAN
my_image.flux
my_image.pb
my_image.mask
my_image.model
my_image.psf
my_image.residual
Relative sky sensitivity
Cleaned and restored image (Jy/clean beam)
Clean “boxes”
Clean components (Jy/pixel)
Dirty beam
Residual (Jy/dirty beam)
Minimally:
If CLEAN is started again with same image name, it will try to continue deconvolution from where it left off. Make sure this is what you want. If not, give a new name or remove existing files with rmtables(‘my_image.*’)
Also: try NOT to do CTRL+C as it could corrupt your MS when it touches the visibilities in a major cycle.
Notes: 101

## Slide 102: Multi-scale CLEAN
multi-scale
“classic” scale
Instead of delta functions, one can use extended clean components
to better match emission scales (multiscales, typically paraboloids)
Pick delta function, half the largest emission and a few in between

## Slide 103: Your ALMA Project (25%)
CASA is the primary software for ALMA DR
It is used for calibration and imaging, which are separate steps
we will only be dealing with imaging, i.e., CLEAN and its nuances
We will utilize CASA guides for ALMA
https://casaguides.nrao.edu/index.php/ALMAguides

## Slide 105: Self Calibration
a priori calibration not perfect
  interpolated from different time, different sky direction from source
basic idea of self calibration
  correct for antenna-based errors together with imaging
works because
  at each time, measure N complex and N(N-1)/2 visibilities
  source structure represented by small number of parameters
  highly overconstrained problem if N large and source simple
in practice, an iterative, non-linear relaxation process
  assume initial model  solve for time dependent gains  form new sky model from corrected data using e.g. CLEAN  solve for new gains…
  requires sufficient signal-to-noise ratio for each solution interval
loses absolute position information
dangerous with small N, complex source, low signal-to-noise

## Slide 106: Summary
Calibrated Visibilities
 Fourier Transform
Dirty Beam and Dirty Image
 Deconvolution
Clean Beam, Sky Model, “restored” Image
 Analysis
Physical Information on Source

## Slide 107: Concluding Remarks
interferometry samples visibilities that are related to a sky brightness image by the Fourier transform
deconvolution corrects for incomplete sampling
remember… there are usually an infinite number of images compatible with the sampled visibilities
astronomer must use judgement in imaging process
imaging is fun (compared to calibration), so that’s what we’re going to focus on for the assignment

## Slide 108: References
Thompson, A.R., Moran, J.M. & Swensen, G.W. 1986, “Interferometry and Synthesis in Radio Astronomy” (New York: Wiley); also 2nd edition
NRAO Summer School proceedings
  http://www.aoc.nrao.edu/events/synthesis/
  Perley, R.A., Schwab, F.R. & Bridle, A.H., eds. 1989, ASP Conf. Series 6, Synthesis Imaging in Radio Astronomy (San Francisco: ASP)
    Chapter 6: Imaging (Sramek & Schwab), Chapter 8: Deconvolution (Cornwell)
  Lecture by T. Cornwell 2002, Imaging and Deconvolution
  Lecture by S. Bhatnagar 2004, Imaging and Deconvolution
IRAM Summer School proceedings
  http://www.iram.fr/IRAMFR/IS/archive.html
  Guilloteau, S., ed. 2000, “IRAM Millimeter Interferometry Summer School”
    Chapter 13: Imaging Principles, Chapter 16: Imaging in Practice (Guilloteau)
  Lecture by J. Pety 2004 “Imaging, Deconvolution & Image Analysis”
(Sub)Millimetre Observing Techniques Summer School
  http://www.mmschool2006.astrosci.ca/

## Slide 109: Missing Low Spatial Frequencies (I)
Large Single Telescope
  make an image by scanning across the sky
  all Fourier components from 0 to D sampled, where D is the telescope diameter (weighting depends on illumination)
  Fourier transform single dish map = T(x,y)  A(x,y), then divide by a(x,y) = FT{A(x,y)}, to estimate V(u,v)
  choose D large enough to overlap interferometer samples of V(u,v) and avoid using data where a(x,y) becomes small
density of uv points
(u,v)

## Slide 110: Missing Low Spatial Frequencies (II)
separate array of smaller telescopes
  use smaller telescopes observe short baselines not accessible to larger telescopes
  shortest baselines from larger telescopes total power maps
ALMA with ACA
64 x 12 m: 12 to 14000 m
+12 x 7 m: fills ~7 to 12
+ 4 x 12 m: fills 0 to ~7

## Slide 111: Missing Low Spatial Frequencies (III)
mosaic with a homogeneous array
  recover a range of spatial frequencies around the nominal baseline b using knowledge of A(x,y) (Ekers and Rots 1979) (and get shortest baselines from total power maps)
  V(u,v) is linear combination of baselines from b-D to b+D
  depends on pointing direction (xo,yo) as well as (u,v)
  Fourier transform with respect to pointing direction (xo,yo)
(u,v)