## Slide 1: Basics of Radio Astronomy
Dr. James Di Francesco - NRC Herzberg Research Centre
(thanks to Sean Dougherty)

## Slide 2: References
Kraus: Radio Astronomy
Wilson, Rohlfs & Huttemeister: Tools of Radio Astronomy*
Stanimirovic, Altschuler, Goldsmith & Salter: Single-dish radio astronomy: techniques & applications
Condon & Ransom: Essential Radio Astronomy✚
*Free e-book available by request
✚Online at http://www.cv.nrao.edu/~sransom/web/xxx.html

## Slide 3: A brief history of wavelength coverage
What we know of the universe is by observation
  Detection and analysis of EM radiation from the universe
Up to 1930 – observations (knowledge) from 0.35 microns  1 micron
1931 – Jansky observes the sky at 14.6m (20 MHz)
1937 – Reber observes at 1.87m (160 MHz)
Radar research during the war – improved antenna/receiver systems
Since 1945:
  interferometry: VLA, MERLIN, VLBA, DRAO, ATCA etc.
  extend to sub-mm: JCMT, CSO
  mm interferometry: PdB, SMA, CARMA, ALMA
  Balloons, aircraft, satellites for l where atmospheric opacity is high.
    EINSTEIN, IUE, IRAS, ISO, MSX, CHANDRA, XMM, SPITZER…..
  ~diffraction limited and interferometry in the optical
Experimental techniques are now mature at almost all wavelengths
  Observations at each wavelength range used as astrophysical tools

## Slide 4: Radio signals – how much energy?
Telescope of area 10,000 m2
Bandwidth = 50 MHz
Flux = 1 mJy
Total energy received in 1000 yrs = 1 erg = 10-7 Joules
~ few percent of energy of a falling snowflake !

## Slide 5: Atmospheric Windows
oxygen ~ 60 GHz ( 5mm) and 119 GHz (2.52 mm)
Radio window --- 5-10 MHz (~30 m)  1000 GHz (300 microns)
- 5 decades of frequency!
Windows defined by absorption by atmospheric molecules
water
  best to pick telescope sites where water content is lower!
  e.g. Mauna Kea, Chajnantor, South Pole.
nitrogen and carbon dioxide absorption --- infrared region.
at low frequencies – cut-off defined by the plasma frequency of the electrons in the ionosphere.

## Slide 6: Radio Frequency Interference (RFI)
VLA 1.2-1.8 GHz

## Slide 7: RFI mitigation techniques 101
No digital switching devices in the telescope beam!
No transmitters in the telescope beam!

## Slide 8: What is detected at radio frequencies?

## Slide 9: What is detected at radio wavelengths?
    Dust emission
  Non-thermal emission
    magneto-bremsstrahlung (gyro emission)
      Cyclotron (non-relativistic)
      Gyro-synchroton (mildly relativistic)
      Synchrotron (highly relativistic)
Continuum emission
  Thermal emission
    bremsstrahlung (free-free emission)

## Slide 10: Continuum emission
Characterized by power-law spectra
Thermal spectrum

## Slide 11: Continuum emission
Characterized by power-law spectra
Non-thermal spectrum

## Slide 12: Thermal emission: HII regions

## Slide 13: Thermal emission: Dust in molecular clouds
Herschel observations of NGC 7538
Composite of 70 μm, 160 μm & 250 μm

## Slide 14: Non-thermal emission: Galactic Centre
Kassim, LaRosa, Lazio & Hyman, 1999

## Slide 15: Non-thermal emission: polarization
NOAO Optical+Ha image www.noao.edu
Radio Continuum
Lines=Magnetic Field Orientation
Beck, Horellou, Neininger www.nrao.edu/imagegallery

## Slide 16
From the wonders of well sampled data….
27-image mosaic of the Cygnus region from DRAO: thermal (blue) non-thermal (red)

## Slide 17: Line Emission
Line Emission -- due to quantum state transitions
  Radio “recombination” lines - high-energy level transitions
  Molecular transitions – rotation & vibration modes
  Hyperfine splitting  21 cm spin-flip of hydrogen
  Maser emission – population inversion (non-thermal)
Line analysis gives:
  Gas characteristics – density, temperature, column density, opacity, abundances, chemistry
  Dynamics: Line-of-sight velocity via Doppler shift
    Infall, outflow

## Slide 18: Molecular Lines
Many molecules discovered in space
  Around 200 detected and counting
Transitions are mainly in the mm/sub-mm
Köln Molecule List – many more than shown here!

## Slide 19: Molecular lines: outflows
Blue=Towards us
Red=Away from us
Chandler & Richer 2001 (SiO J=1-0 in HH 211)
outflow in S106

## Slide 20: Molecular Lines: dynamics
Text

## Slide 21: Molecular lines: maser emission
VLBA observations of SiO maser emission in wind of AGB star
Gas motions are evident
The “ring” diameter ~10AU
73-epochs of SiO maser observations of TX Cam (Gonidakis and Diamond)

## Slide 22: Neutral Hydrogen in Galaxies
NGC 6946

## Slide 23: HI: dynamics of our own Galaxy
HI4PI movie
https://www.youtube.com/watch?v=Q2mgpsTFuV8

## Slide 24: (just a reminder)
Some basic concepts

## Slide 25: Basic Concepts
EM power in bandwidth dn from solid angle dW intercepted by surface dA is:
Defines surface brightness Iv (W m-2 Hz-1 sr-1) ( aka intensity/specific intensity)
Note:
Flux density Sv (W m-2 Hz-1) – integrate brightness over solid angle of source
Convenient unit - the Jansky  1 Jy = 10-26 W m-2 Hz-1 = 10-23 erg cm-2 Hz-1

## Slide 26: Surface Brightness of a Black body
Surface brightness of a black body defined by the Planck Function
Radiation emitted at n depends only on n and the blackbody temp T
Special case – Rayleigh-Jeans limit
This approximation starts to break down in mm

## Slide 27: Surface Brightness
In general surface brightness is position dependent ie. In=In(q,f)
i.e. surface brightness is described by a temperature distribution
Back to flux:
In general, a radio telescope maps the temperature distribution of the sky

## Slide 28: Brightness Temperature
Many astronomical sources DO NOT emit as blackbodies!
However….
Brightness temperature (TB) of a source is defined as the temperature of a blackbody with the same surface brightness of a source at a given frequency.
This implies that the flux density

## Slide 29: Brightness Temperature
Examples:
‘Blank’ Sky 2.73 K Big Bang
Orion Nebula @ 300 GHz 10-100 K Warm molecular cloud
Orion Nebula @ 1 GHz 104 K Thermal
Quasar 107-12 K Synchrotron
‘Quiet’ Sun @ 300 MHz 5x105 K Synchrotron
Sun @ 30 GHz 5800 K Thermal
@ 30 GHz T~5800 K
=> Thermal emission
@ 300 MHz T~106 K
=> Non-thermal emission

## Slide 30: Tools of the trade - telescopes

## Slide 31: Telescopes – our eyes on the Universe
Most of what we know of our universe is through detection of electromagnetic radiation.
The purpose of an astronomical telescope is to determine the characteristics of this emission:
  Angular distribution
  Frequency distribution
  Polarization characteristics
  Temporal characteristics
Telescopes
  imperfect devices
  their efficient use requires an understanding of their capabilities and limitations.

## Slide 32: Radio telescopes
Radio regime spans a vast range of wavelength
Very different instruments to span this range
l > 1 m (=300 MHz) – wire antennas

## Slide 33: Radio telescopes
l ~ 1 m -- hybrid antennas (wire reflectors or feeds)
l < 1 m -- reflector antennas
Radio regime spans a vast range of wavelength
Very different instruments to span this range
l > 1 m (=300 MHz) – wire antennas
Single telescopes
Multi-element arrays (interferometers)
- see upcoming lecture by Brenda Matthews

## Slide 34: An example of a single dish – the GBT
100m diameter
largest fully steerable telescope in the world
surface rms ~ 360mm
100m
ALMA -12m diameter
surface rms ~ 25mm

## Slide 35: Radio telescope systems
Radio telescopes are devices for generating an electrical signal from incoming EM radiation
Astrophysical radio signals are typically weak compared to background “noise”
Radio telescopes have to be:
  highly directional (aka high gain)
    dependent on antenna beam/power pattern
  Extract energy from the incoming wavefront
    Antenna size
    Antenna Efficiency
Receivers - convert EM signal to a voltage - amplify the “noise”
Back end (correlator/power detector) - to detect the signal

## Slide 36
Signal path:

## Slide 37: Reflector Types
Prime focus Cassegrain focus
(GMRT) (ATCA,JCMT,ALMA)
Offset Cassegrain Nasmyth
(VLA) (OVRO, JCMT)
Beam Waveguide Dual Offset
(NRO) (ATA)

## Slide 38
Newton’s comments on the Cassegrain design:
“….You see therefore, that the advantages of this design are none; but the disadvantages so great and unavoidable that I fear it will never be put in practice with good effect”
Phil. Trans. Royal. Soc. London. 7, 4056 (1672)

## Slide 39: Useful telescope characteristics

## Slide 40
The antenna collects the E-field over the aperture at the focus
The feed horn at the focus adds the fields

## Slide 41: Beam Pattern - origin
An antenna’s response is a result of incoherent phase summation at the focus.
First null occurs at the angle where the extra distance for a wave at center of antenna is in anti-phase with that from edge.
(D/2) sin q = l/2
q ~ l/D
On-axis
incidence
Off-axis
incidence
Larger D => interferometers
(see Brenda’s lecture)
For a given wavelength, the larger D, the higher resolution
D ~ 100 m ; e.g., GBT

## Slide 42: Antenna power pattern
“Power pattern" P(q,j) of a telescope is the square of the complex far-field voltage pattern F(l,m) i.e. |F(l,m)|2 = F(l,m)F*(l,m).
(diffraction theory -- voltage pattern F(l,m) is the FT of the aperture distribution )
Defines telescope resolution

## Slide 43: Beam sizes
Small beams – need good and stable pointing – IMPORTANT @ mm l
2’
100 m
GBT
q
D
0.001”
8611 km
VLBA
0.06”
215 km
MERLIN
0.34”
36 km
VLA
8’
25 m
VLA dish
cm telescopes @ 5 GHz
mm telescopes @ 345 GHz
q (“)
D
0.35
508 m
SMA
4.5
50 m
LMT
15
15 m
JCMT
103
1.7 m
AST/RO
0.012
15 km
ALMA

## Slide 44: The Beam
The antenna “beam” solid angle on the sky is:
Sidelobes
NB: rear lobes!

## Slide 45: The Beam
The antenna “beam” solid angle on the sky is:
Antenna gain (aka directivity) - a measure of how big the beam is on the sky:
Antenna design aims to minimize WA to maximize antenna gain
  e.g., dipole antenna – low gain; parabolic reflector – high gain

## Slide 46: Antenna efficiency
Effective aperture Ae of an aperture A :
(h = the aperture efficiency)
Antenna theorem relates Ae and WA :
As effective area increases, solid angle of beam decreases
  “gain” increases
Increasing Ae increases sensitivity - nice to have!
Not possible to have large Ae for sensitivity (and gain) with a large beam (to see more sky)

## Slide 47: Antenna Efficiency II
Aperture Efficiency h = hsurface ´ hblockage ´ hspill ´ htaper ´ hmisc
hsurface = reflector surface efficiency ~ exp(-(4ps/l)2)
=> if s = l/20 , hsur = 0.67
hblockage = blockage efficiency
hspill = feed spillover efficiency
htaper = feed illumination efficiency
hmisc = diffraction, phase errors due to feed position etc
l cm | hsur | hbl | hspill | htap | hdiff | hmis | htot
20 | 1.0 | 0.85 | 0.82 | 0.98 | 0.86 | 0.94 | 0.55
6 | 0.97 | 0.85 | 0.92 | 0.98 | 0.96 | 0.94 | 0.67
2 | 0.85 | 0.85 | 0.90 | 0.95 | 0.98 | 0.94 | 0.57
1.3 | 0.68 | 0.85 | 0.90 | 0.95 | 0.98 | 0.94 | 0.46
l mm | hsur
2.6 | 0.79
1.3 | 0.75
0.87 | 0.70
0.65 | 0.63
0.44 | 0.48
VLA s = 650 mm
ALMA s = 25 mm

## Slide 48: MM telescope – where surface rms rules!
Accurate surface
  Stiff reflector
Enclosed backing structure for thermal stability
  Low surface deformation
Pointing accuracy
very important with small beam
(q ~ l/D)
  15 m => 15” @ 345 GHz
  Enclosed yoke
  Enclose the telescope!

## Slide 49: What are we detecting and how?

## Slide 50: What does a radio telescope detect?
Recall :
Telescope of effective area Ae receives power Prec per unit frequency from an unpolarized source (only sensitive to one mode of polarization)
Telescope is sensitive to radiation from more than one direction with relative sensitivity given by the normalized antenna pattern PN(q,j)

## Slide 51: Antenna temperature
Nyquist theorem (1929):
Antenna temperature is what is observed by the radio telescope
Power received by the antenna:
A “convolution” of sky brightness with the beam pattern
It is an inversion problem to determine the source temperature distribution.

## Slide 52: Antenna temperature: some special case I
Gives a measure of reflector performance
For a point source ie Wbeam >> Wsource : PN (q, j)=1
=> known point source flux density Sn, measure TA to get Ae
e.g., Arecibo 300 m : 0.07Jy/K
JCMT 15 m : ~25 Jy/K

## Slide 53: Antenna temperature: some special case II
Need to know the power pattern
For an extended source ie Wbeam ~ Wsource.
Assume T (q, j)=constant over the beam e.g. the Moon
Main beam filling factor

## Slide 54: Receiver systems
  cm – use heterodyne receivers
Spectral line – need narrow frequency bands
  use heterodyne receivers
    preserve phase information
      essential for interferometry
    Typically a correlator (power detector)
A radio source produces an antenna temperature TA
How do we detect this (perhaps very small e.g. ~ 10-4 -10-7) change in power that appears at the output of the telescope?
The challenge of the receiver (detector) system
Two main types of observation – continuum and spectral line
Continuum – total power is required
  mm/sub-mm -> bolometers – sensitive, wide bandwidths
  SCUBA

## Slide 55: Components of a heterodyne receiver
Amplifier
  Amplify very weak signal
  Needs to be stable and have very low noise
Mixer
  Produces a stable low frequency signal which mixes the higher frequency (RF) signal to a lower, intermediate (IF) frequency.
    Mixer can be tuned to detect a large range of RF
    Cost (samplers, amplifiers, transmission line) and performance (filtering)
    Transmission lines less lossy at lower frequency (optic fibre relief)
Filter – selects a narrow signal band
Backend – either total power detector or more typically today, a correlator
Back end
Power detector/integrator
Correlator

## Slide 56: Backend Example: ACSIS on JCMT
ACSIS = AutoCorrelation Spectral Imaging System
Built by NRC Penticton
Used by JCMT heterodyne receivers
Very configurable with up to 2 or 4 spectral windows depending on receiver used
Spectral resolution varies from 30 kHz to 1 MHz, as needed
Data read out at 0.1 s intervals for fast mapping
HARP configurations:
R = Δλ/λ ~ 10-7 !!

## Slide 57: Noise in the machine!
Unfortunately, the telescope system contributes noise to the source signal detected by the telescope
i.e. Pout = PA + Psys => Tout = TA + Tsys
Tsys represents the noise added by the system
= Tbg [exp(-tau*A)] + Tsky [exp(-tau*A) -1] + Tspill + Tloss + Trx + Tcal ;
where A = airmass ~ 1/sin(elevation) for elevation > 15 degrees,
and tau = opacity at the frequency of interest
Tbg = microwave and galactic background (3 K, except below 1 GHz)
Tsky = atmospheric emission (increases with frequency--dominant in mm)
Tspill = ground radiation (via sidelobes) (telescope design)
Tloss = losses in the feed and signal transmission system (design)
Trx = receiver system (often dominates at cm — a design challenge)
Tcal = injected calibrator signal (usually small)
Note that Tbg,Tsky,Tspill vary with position on the sky
Tsky also is time variable

## Slide 58: System Noise – cm regime
Trx is the challenge!
54
39
34
31
26
JVLA
154
100
7
21
6
17
3
1.3
116
80
6
13
6
8
3
2
30
16
2
2
5
2
3
3.6
50
30
2
5
7
3
3
6
60
30
2
8
14
3
3
20
125
70
5
7
15
3
25
92
Tsys
Trx
Tcal
Tloss
Tspill
Tsky
Tbg
lcm
VLA
=>T1 needs to be small

## Slide 59: System Noise – mm regime
Tsky is the challenge
Trx < Tsky
  Trx is essentially at the quantum limit
<175
602-720
Band 9
<83
275-370
Band 7
<83
211-275
Band 6
<37
84-116
Band 3
Trx K
GHz
ALMA Trx

## Slide 60: Radiometry equation
Challenge: How to detect TA (signal) in the presence of Tsys (noise)?
The signal is correlated from one sample to the next - the noise is not.
For a bandwidth Dn, samples taken less than Dt=1/Dn are not independent
(another Nyquist theorem!)
Time t contains independent samples
Radiometer equation
Gaussian noise : total error for N samples is
that of single sample

## Slide 61: Flux sensitivity & antenna performance
  For a point source, flux density Sn recall
  Minimum detectable flux
  Ae/Tsys is the measure of the performance of a radio telescope

## Slide 62: Flux sensitivity & antenna performance II
cm telescopes
74
40
27
24
31
Tsys
18
4162
100
Bonn
SEFD (Jy)
Ae (m2)
D (m)
@5 GHz
600
338
26
Onsala
300
360
25
VLBA PT
13
7850
100
GBT
3.9
22080
300
Arecibo

## Slide 63: Flux sensitivity & antenna performance II
NEFD (mJy s1/2)
2200
2000
150
79
CSO
200
200
5
SOFIA
54
54
7
FIRST
350 mm
450 mm
850 mm
Ae (m2)
15
12
2
7000
ALMA
1250
1142
134
227
SMA
760
700
107
80
22
177
Scuba
Scuba 2
2660
2300
2160
2
AST/RO
Mm/submm telescopes

## Slide 64: The essential qualities of a radio telescope
Lots of area!
High antenna efficiency
  Good surface rms
Low system temperature
  Low receiver temperature
    Low noise in the 1st stage (LNA – low noise amplifier)
  At mm, Tsky is the challenge
    Low water content above the site
      e.g. Chajnantor, South Pole, Mauna Kea
  All this improves
Receiver bandwidth
  – drives down minimum detected flux
Good pointing – most especially at mm/sub-mm.

## Slide 65: Calibration & Observing Techniques

## Slide 66: What does the telescope measure?
TA = “antenna temperature”
TA(total) = Tsource + Tsys
Tsys represents the noise added by the system
= Tbg [exp(-tau*A)] + Tsky [exp(-tau*A) -1] + Tspill + Tloss + Trx ;
where A = airmass ~ 1/sin(elevation) for elevation > 15 degrees,
and tau = opacity at the frequency of interest
Want Tsource, so carry out ON – OFF
TA(ON) = Tsource + Tsys, TA(OFF) = Tsys, so TA(ON) – TA(OFF) = Tsource
Need to carry out ON – OFF observations, and there are different observing techniques for measuring ON – OFF

## Slide 67: Different Observing Modes to get OFFs
Types of “reference observations”:
Frequency Switching
- In- or Out-of-band
Position Switching
Beam Switching
- Move subreflector
- Receiver beam switch
Dual-beam Nodding
- Move telescope
- Move subreflector

## Slide 68: In-band Frequency Switching

## Slide 69: Out-of-band Frequency Switching

## Slide 70: Position Switching

## Slide 71: Position Switching: ON – OFF on sky

## Slide 72: Beam Switching : Internal (“Dicke”) Switching
Difference spectrum eliminates any contributions to the bandpass from after the switch
Low overhead but ½ time spent off source

## Slide 73: Beam Switching : Subreflector or internal tertiary
Removes “fast” gain / bandpass changes
Low overhead but ½ time spent off source

## Slide 74: Nodding with dual-beam Rx’s - subreflector, etc
Removes “fast” gain / bandpass changes
Low overhead and all time spent on source

## Slide 75: Nodding with dual-beam Rx’s – telescope motion
Removes “fast” gain / bandpass changes
Overhead from moving the telescope but all time spent on source

## Slide 76: Mapping Techniques
Point map
- sit, move, sit, move….
On-The-Fly mapping
- slew a column or a row while collecting data
- move to next column / row
- basket weave
- should oversample ~1/3 the resolution along direction of slew (“Nyquist sampling”)
- OFF position taken from either an emission free map position or a separate OFF position observed

## Slide 77: Data Calibration
(ON – OFF) / OFF
[ (Tsource + Teverything else) – Teverything else ]/ Teverything else
= (source temperature) / (“system temperature”)
TA = [(ON – OFF) / OFF] * Tsys
OFF obtained from observations of blank sky (or other)
Tsys obtained from internal calibration (noise diodes, etc.)

## Slide 78: Determining Tsys with noise diodes
Tsys = [OFF / (ON – OFF)] * Tcal
Tsys = [OFF / (ON – OFF)] * Tcal + Tcal/2
(Used at GBT for Flicker diode ON/OFF)
GBT uses noise diodes for all receivers except 4 mm one and MUSTANG bolometer array

## Slide 79: Determining Tsys with hot / cold loads
“calibration gain” G = (Thot – Tcold) / (Vhot – Vcold) [K/Volts]
Tsys = G * V(OFF) and TA = G * (ON-OFF)
GBT uses hot/cold loads for 4 mm receiver
One load “chopper wheel” method also used! See Kutner & Ulich (1974)

## Slide 80: Absolute Calibration on known sources
Corrects for errors in adopted diode temps, etc., and corrects for telescope response
S(source) / S(cal) = T(source) / T(cal), where S(cal) is known, e.g., 3C273, planet…
VLA calibration is ~1% accurate at < 20 GHz and ~3% accurate at > 20 GHz
Mars WMAP observations with model in red

## Slide 81: Temperature Scales in Radio Astronomy
TA ; observed source antenna temperature
TA’ = TA exp (tau * A) ; antenna temperature corrected for atmospheric opacity tau at airmass A
; ηr = radiation efficiency of telescope (ohmic losses due to resistive heating)
TA* = TA’ / ηrηrss. ; ηrss = rearward scattering/spillover efficiency
; ηl = ηrηrss = fraction of power in forward direction
TR* = TA’ / ηlηfss ; ηrss = forward scattering/spillover efficiency
Tmb = TA’ / ηmb ; main-beam temperature, where ηmb = fs ηc(main beam) ηfss , fs = source filling factor, and ηc(main beam) = coupling of source that just fills the main beam (Mangum 1993, 2006)
ηa ~ ηmb ./ 1.3 for GBT = Ae / A ; “aperture efficiency”

## Slide 82: And to close….
Some gratuitous images of telescopes

## Slide 83: At cm - the VLA
Featured in the movie ‘Contact’.
World’s ‘largest’ array.
27 “movable” antennas
25 m diameter each
Total area = 130-m diameter dish
Y configuration (“2D” array)
Longest baseline = 36 km

## Slide 84
In the year 2018……

## Slide 85: At mm/sub-mm…
IRAM
LMT

## Slide 86: At mm/sub-mm…
CARMA
ALMA

## Slide 87
Arecibo
FAST